## Slide 1: Network Topologies
Topic 6A

## Slide 2: Learning Outcomes
By the end of this lesson, you should be able to:
Describe the primary physical networking topologies in common use
Describe the primary logical networking topologies in common use
Describe major LAN networking technologies
Compare Wi-Fi standards

## Slide 3: Physical Topologies
The word “topology” describes the lay of the land
A network topology describes how a network is physically laid out and how signals travel from one device to another
The physical layout of the devices and cables doesn’t describe how signals travel from one device to another
  Network topologies are categorized into physical and logical topologies
The arrangement of cabling and how cables connect one device to another in a network is considered the network’s physical topology
The path data travels between computers on a network is considered the network’s logical topology
All network designs today are based on these basic physical topologies: bus, star, ring, and point-to-point

## Slide 4: Physical Bus Topology
Physical bus topology is defined as a continuous length of cable connecting one computer to another in daisy-chain fashion
  The simplest and at one time the most common method for connecting computers
Weaknesses
  There’s a limit of 30 computers per cable segment
  The maximum total length of cabling is 185 meters
  Both ends of the bus must be terminated
  Any break in the bus brings down the entire network
  Adding or removing a machine brings down the entire network temporarily
  Technologies using this topology are limited to 10 Mbps half-duplex communication since they use coaxial cabling
Due to the limitations, this topology is no longer a practical choice and technology has moved past this obsolete method of connecting computers

## Slide 5: Physical Bus Topology

## Slide 6: Physical Bus Topology
How Data Travels in a Physical Bus
  Electrical pulses (signals) travel the cable’s length in all directions
  Signals travelling across the medium and from device to device is called signal propagation
  The signal continues until it weakens or is absorbed by a terminator
    A terminator is an electrical component called a resistor that absorbs the signal instead of allowing it to bounce back up the wire
  If not terminated, the signal bounces or is “reflected” at end of medium
    Signal bounce is the term used when electricity bounces off the end of a cable and back in the other direction

## Slide 7: Physical Bus Topology
Physical Bus Limitations
  Only 30 computers can be daisy-chained together before signal becomes too weak to be passed along to another computer
  As an electrical signal encounters each workstation along a daisy-chain,
    Some of its strength is absorbed by both the cabling and the connectors until the signal is too weak for a NIC to interpret
  For the same reason, total length of cabling is limited to 185 meters
  Has a maximum bandwidth of 10 Mbps half-duplex communication
    Due to use of coaxial cable

## Slide 8: Physical Star Topology
Uses a central device (hub or switch) to connect computers
  Each computer has a single length of cable going from its NIC to the central device
Advantages:
  Much faster technologies than a bus
  Centralized monitoring and management of network traffic are possible
  Easier network upgrades
Using a central device allows for monitoring and managing a network
  Hubs and switches can include software that collects statistics about network traffic patterns and detect errors
  As long as cabling and NICs support it, a star network can be easily updated by replacing the central device
When the number of workstations you need exceed the number of ports on a central device you simply add another central device

## Slide 9: Physical Star Topology

## Slide 10: Physical Star Topology
Extended Star
  The extended star topology is the most widely used in networks containing more than just a few computers
  A central device (usually a switch) sits in the middle and instead of attached computers, other switches or hubs are connected to the central switch’s ports
    Computers and peripherals are then attached to these switches or hubs forming additional stars
  Sometimes referred to as a “hierarchical star”
  This topology is most effective when the center of the star is running at a much faster speed than other devices

## Slide 11: Physical Star Topology

## Slide 12: Physical Star Topology
How Data Travels in a Physical Star
  Details of how data travels in a physical start depend on the type of central device
  The central device determines ‘logical’ topology
    Logical topology is discussed later in the chapter
    For now: hub = logical bus; switch = logical switching; MAU = logical ring
Physical Star Disadvantages
  There are many advantages of a physical star
  The main disadvantage is that the central device represents a single point of failure
    If the hub or switch fails or someone kicks the power cord out of the outlet, the entire network goes down
    Having a spare on hand is a good idea

## Slide 13: Physical Ring Topology
A physical ring topology is like a bus:
  Devices are daisy-chained one to another
  Instead of terminating each end, the cabling is brought around from the last device back to the first device to form a ring
This topology was most widely used to connect LANs with a technology called Fiber Distributed Data Interface (FDDI)
  FDDI was most often used as a network backbone, which is cabling used to communicate between LANs or between hubs and switches
Data travels in one direction
  If any station in the ring fails, data can no longer be passed along
FDDI uses a dual ring, which means:
  Data travels in both directions
  One ring failure doesn’t break network
Extended star topologies with Gigabit Ethernet has largely replaced FDDI

## Slide 14: Physical Ring Topology

## Slide 15: Point-to-Point Topology
A point-to-point topology is a direct link between two devices
  Mostly used in WANs
Advantage of this topology:
  Data travels on a dedicated link and bandwidth is not shared with other networks
Disadvantage of this topology:
  Expensive
Point-to-point technologies are used with wireless networks as a wireless bridge
  This setup can be used to connect two buildings without using a wired network
Can also be used to connect two computers together for transferring files

## Slide 16: Point-to-Point Topology

## Slide 17: Point-to-Point Topology
Point-to-Multipoint Technology
  Point-to-multipoint (PMP) topology is an arrangement where a central device communicates with two or more other devices
    All communication goes through the central device
  It is often used in WANs where a main office has connections to several branch offices via a router
    A single connection is made from the router to a switching device that directs traffic to the correct branch office
  Also used in wireless network arrangements
    A single base station communicates with multiple subscriber stations

## Slide 18: Point-to-Point Topology

## Slide 19: Point-to-Point Topology
Mesh Topology
  A mesh topology connects each device to every other device in a network
    Multiple point-to-point connections for the purposes of redundancy and fault tolerance
  The purpose of creating a mesh topology is to ensure that if one or more connections fail, there’s another path for reaching all devices on the network
  Found in large WANs and internetworks
  It is expensive due to multiple interfaces and cabling

## Slide 20: Point-to-Point Topology

## Slide 21: Logical Topologies
A network’s logical topology describes how data travels from computer to computer
Sometimes same as physical topology
  In a physical bus and physical ring, the logical topology mimics the physical arrangement of cables
  For physical star, electronics in central device determine logical topology
A logical ring using a physical star implements the ring inside the central device’s electronics, which is a MAU in the token ring technology
In a switched topology, there is always an electrical connection between the computer and the switch
  But when no data is being transferred there is no logical connection or circuit between the devices

## Slide 22: Logical Topologies

## Slide 23: Logical Topologies

## Slide 24: Logical Topologies

## Slide 25: Network Technologies
Network technology is the method a network interface uses to access the medium and send data frames and the structure of these frames
Other terms:
  Network interface layer technologies
  Network architectures
  Data link layer technologies
A network uses Ethernet, 802.11 wireless, or some combination of these to move data from device to device in your network
WAN examples include
  Frame relay, SONET, and ATM
The network technology often defines frame format and media

## Slide 26: Network Technologies and Media
Unshielded Twisted Pair
  Unshielded twisted pair (UTP) is the most common media type in LANs
  Consists of 4 pairs of copper wires
  each twisted together
  Comes in numbered categories
    The higher the number, the higher the cable’s bandwidth potential
Fiber-optic Cabling
  Fiber-optic cabling uses thin strands of glass to carry pulses of light long distances and at high data rates
  Isn’t susceptible to electrical interference
Coaxial Cable
  Coaxial cable is obsolete as a LAN medium but it is used as the network medium for Internet access via cable modem

## Slide 27: Network Technologies and Media
Baseband and Broadband Signaling
  Network technologies can use media to transmit signals in two main ways
  Baseband sends digital signals in which each bit of data is represented by a pulse of electricity or light
    Sent at a single fixed frequency and no other frames can be sent along with it
  Broadband uses analog techniques to encode binary 1s and 0s across a continuous range of values
    Signals flow at a particular frequency and each frequency represents a channel of data

## Slide 28: Ethernet Networks
Ethernet is the most popular LAN technology
  Advantages include ease of installation, scalability, media support, and low cost
It supports a broad range of speeds: 10 Mbps to 10 Gbps
Ethernet can operate a in physical bus or physical star and logical bus or switched logical topology
Most NICs/hubs/switches can operate at multiple speeds: 10/100/1000
  Underlying technology is the same, regardless of speed

## Slide 29: Ethernet Networks
Ethernet Addressing
  Every station has a physical (MAC) address
  Each MAC address has 48 bits expressed as 12 hexadecimal digits
  Incoming frames are read for the destination MAC address and to see if they match the NIC’s own MAC address
  If they match or if the destination address is the broadcast MAC address:
    Incoming frames are sent to the network protocol for further processing

## Slide 30: Ethernet Networks
Ethernet Frames
  A frame is the unit of network information that NICs and switches work with
  Frames must be between 64 and 1518 bytes and consist of the following:
    A 14-byte frame header composed of these three fields:
      Destination MAC (6 bytes)
      Source MAC (6 bytes)
      Type (2 bytes)
    Data field from 45 to 1500 bytes
    A frame trailer (frame check sequence [FCS]) of 4 bytes

## Slide 31: Ethernet Networks

## Slide 32: Ethernet Networks
Ethernet Media Access
  Media access method is a set of rules governing how and when the medium can be accessed for transmission
  Ethernet uses Carrier Sense Multiple Access with Collision Detection (CSMA/CD)
    Carrier Sense: Listen before send – must hear silence
    Multiple Access: If two or more stations hear silence, multiple stations may transmit at the same time
    Collision Detection: If two or more stations transmit, a collision occurs and is detected by the NIC; all stations must retransmit

## Slide 33: Ethernet Networks
Collisions and Collision Domains
  All devices interconnected by one or more hubs hear all signals generated by all other devices
  The extent to which signals in an Ethernet bus topology network are propagated is called a collision domain
  All devices in a collision domain are subject to the possibility that whenever a device sends a frame, a collision might occur

## Slide 34: Ethernet Networks

## Slide 35: Ethernet Networks
Ethernet Error Handling
  Ethernet is a best-effort delivery system
    There’s no acknowledgement or verification that the frame arrived at its intended destination
  Ethernet relies on network protocols to ensure delivery
  Ethernet detects damaged frames
    The error-checking code in an frame’s trailer is called a Cyclic Redundancy Check (CRC)
    Ethernet uses the CRC to determine that data is unchanged
    If a frame is detected as damaged, it is discarded with no notification

## Slide 36: Ethernet Networks
Half-Duplex versus Full-Duplex Communication
  Half-duplex works like a two-way radio; you can talk and listen but not both at the same time
    Ethernet on hubs works only in half-duplex
  Full-duplex means NIC/switch can transmit/receive simultaneously
    CSMA/CD is not used because a collision cannot occur in full-duplex mode
    Most switches operate in full-duplex

## Slide 37: Ethernet Standards
Standards Terminology
  Ethernet standards expressed in one of two ways:
  Using the IEEE document number defining the standard (IEEE 802.3)
  XBaseY – 10BaseT, 100BaseT, 100BaseFX
    X – designates the speed of transmission
    Y – specifies the type of media (T = twisted-pair, FX = fiber optic)
10BaseT Ethernet
  Uses two of the four wire pairs
  Runs over Category 3 or higher UTP cabling
  Highly susceptible to collisions and is obsolete

## Slide 38: Ethernet Standards
100BaseTX Ethernet
  Most common Ethernet variety
  Runs over Category 5 or higher UTP
  Uses two of four wire pairs
  Also sometimes called “Fast Ethernet”
100BaseFX Ethernet
  Runs over two strands of fiber optic cabling
  Typically used as backbone cabling between hubs or switches
    Also used to connect clients or servers when immunity to noise and eavesdropping is required

## Slide 39: Ethernet Standards
1000BaseT Ethernet
  Usually called “Gigabit Ethernet”
  Runs over Category 5e or higher UTP and uses all four wire pairs
  To support full-duplex transmission over a single pair of wires:
    1000BaseT uses hybrid and canceller technology, which combines multiple signals and cancels interference
2.5GBaseT and 5GBaseT
  This specification was largely in response to increasing Wi-Fi speeds
  Faster wired Ethernet speeds are needed as uplink ports from new 802.11ac APs
  Runs over Cat 5e/6 cabling

## Slide 40: Ethernet Standards
10GBaseT Ethernet
  Runs over four pairs of Category 6A or 7 UTP
  Operates only in full-duplex mode
    No hubs, only switches support 10GBaseT
  Still considered an expensive option, although prices are dropping
  Good for network servers so they can keep up with desktop systems that commonly operate at 1 Gbps

## Slide 41: Additional Ethernet Standards
100BaseT4
  Uses all four pairs of wires in UTP Category 3 cable
  Obsolete
1000BaseLX
  Uses fiber-optic media
  “L” stands for “long wavelength” laser
  Supports a maximum cable segment length of 5000 meters
    Some manufacturers have extended it by using specialized and proprietary optical transceivers

## Slide 42: Additional Ethernet Standards
1000BaseSX
  Uses fiber-optic media
  “S” stands for “short wavelength” laser
  Can’t cover as much distance as long-wavelength lasers, but are less expensive
1000BaseCX
  Uses specially shielded, balanced, copper jumper cables
  Might also be called “twinax” or “short-haul” copper cables

## Slide 43: Additional Ethernet Standards
10 Gigabit Ethernet IEEE 802.3ae Standards
  Much like the others in frame formats and media access
  Defined to run only on fiber-optic cabling and specifies a maximum distance of 40 kilometers
  Primarily used for network backbones
  Varieties:
    10GBaseSR, 10GBaseLR, 10GBaseER, 10GBaseSW, 10GBaseLW, and 10GBaseEW

## Slide 44: Additional Ethernet Standards
40 Gigabit and 100 Gigabit Ethernet
  Very high cost is still prohibitive
  Adoption has been slow
  Fiber-optic cabling is primary medium
    Although there are provisions to use special copper assemblies over short distances
What’s Next for Ethernet?
  Estimations are that Ethernet speeds will continue to increase
    With Terabit Ethernet (1000 Gbps) as part of the discussion
  Work on a 200 and 400 Gbps standard was completed in 2017
    Devices are not yet readily available

## Slide 45: 802.11 Wi-Fi
The 802.11 wireless networking standard is also referred to as Wireless Fidelity (Wi-Fi)
In most towns you can usually find a public Wi-Fi network, called a hotspot
802.11 is essentially an extension to Ethernet
  Using airwaves instead of cabling as the medium

## Slide 46: Wi-Fi Modes of Operation
Wi-Fi can operate in one of two modes
  Infrastructure mode use a central access point (AP)
    Stations connect through a wireless AP before they can communicate with other devices
  Ad hoc mode is a mode of operation where there is no central device
    Data travels from device to device like a bus
    Sometimes called “peer-to-peer mode”
Most of this chapter’s discussion of Wi-Fi focuses on infrastructure mode

## Slide 47: Wi-Fi Channels and Frequencies
Wi-Fi networks operate at one of two radio frequencies: 2.4GHz and 5.0 GHz
  Although this frequency is not fixed
2.4 GHz is actually 2.412 thru 2.484 divided into 14 channels spaced 5 MHz apart
5.0 GHz is actually 4.915 thru 5.825 GHz divided into 42 channels of 10, 20, or 40 MHz each
A wireless channel works like a TV channel:
  You must tune to the correct channel to connect
If you are configuring several Wi-Fi networks:
  Choose channels five apart from other known APs

## Slide 48: Wi-Fi Channels and Frequencies

## Slide 49: Wi-Fi Antennas
The antenna on a Wi-Fi device is both transmitter and receiver
  Characteristics and placement determine how well a device transmits or receives Wi-Fi signals
Antennas are usually categorized by their radiation pattern:
  Omnidirectional antennas – signals radiate out from the antenna with equal strength in all directions
  Unidirectional antenna – signals are focused in a single direction
    Ideal for placement at one end of long, narrow spaces

## Slide 50: Wi-Fi Antennas

## Slide 51: Wi-Fi Access Methods and Operation
Wi-Fi Access Method
  Sending station can’t hear if another station begins transmitting so they cannot use the CSMA/CD access method that Ethernet uses
  Wi-Fi devices use Carrier Sense Multiple Access with Collision Avoidance (CSMA/CA)
  802.11 standards specify a feature that uses handshaking before transmission
    Uses request-to-send/clear-to-send (RTS/CTS) packets and acknowledgements
  The 802.11b standard specifies a transmission rate of 11 Mbps
    But this value is not absolute
    Environmental conditions prevent transmission at this speed

## Slide 52: Wi-Fi Signal Characteristics
Common types of signal interference caused by physical objects:
  Absorption – solid objects absorb radio signals, causing them to attenuate (weaken)
  Refraction – the bending of a radio signal as it passes from a medium of one density through a medium of a different density
  Diffraction – the altering of a wave as it tries to bend around an object
  Reflection – occurs when a signal hits a dense, reflective material, resulting in signal loss
  Scattering – when a signal changes direction in unpredictable ways, causing a loss in signal strength

## Slide 53: Wi-Fi Signal Characteristics
Signal-to-noise ratio is the amount of noise compared with the signal strength
  Noise can come from equipment, other wireless devices, and other wireless networks
Throughput is the actual amount of data transferred
  Not counting errors and acknowledgements
Goodput is actual application-to-application data transfer speed
Packet frame headers, acknowledgements, and retransmissions are collectively known as overhead

## Slide 54: Wi-Fi Standards
Advantages and disadvantages of each standard:
  802.11a – requires more power and has a shorter indoor range, transfers data at 54 Mbps
  802.11b – was the most widely accepted standard because of its low cost and good indoor range
    Because it operates at only 11 Mbps, 802.11g and 802.11n have rapidly replaced it
  802.11g – 2.4 GHz standard that is backward-compatible with 802.11b
    Suffers from the same interference problems as 802.11b networks
  802.11n – adds multiple-input/multiple-output (MIMO) antennas
    MIMO takes advantage of multipath signals by using a separate antenna to process signals as they arrive slightly out of phase

## Slide 55: Wi-Fi Standards
Advantages and disadvantages of each standard (continued):
  802.11ac – operates in the 5.0 GHz range only and can support data rates up to 1 Gbps
    Future implementations will have speeds up to 6.93 Gbps
    Improves on the MIMO technology by providing up to eight data streams and introducing multiuser MIMO (MU-MIMO), which allows APs to send data to multiple client stations simultaneously
  802.11ax – a work in progress that promises speeds up to 10 Gbps and will possible operate in the 1 GHz and 7 GHz frequency bands
    Has been dubbed Wi-Fi 6, with 802.11ac being referred to as Wi-Fi5, and 802.11n is now called Wi-Fi 4

## Slide 56: Wi-Fi Security
Signals from a Wi-Fi network can travel several hundred feet – Wi-Fi devices outside your home or business can detect your signals
Wi-Fi network should be protected by an encryption protocol that makes data difficult to interpret
Encryption protocols
  Wired equivalent privacy (WEP), Wi-Fi Protected Access (WPA), and WPA2,
  Not all devices support all three protocols
    Older devices might only support WEP and/or WPA
Wi-Fi encryption is configured on the AP

## Slide 57: Token Ring Networks
Based on the IEEE 802.5 standard
Token Ring networks are cabled in a star physical topology but function as a logical ring topology
Originally operated at 4Mbps and then increased to 16 Mbps and later 100 Mbps
Uses cat 4 and higher UTP
Token Ring Media Access
  A token is passed along the network
    Only the station with the token can transmit
    Frames are acknowledged and token is released
    No collisions
Token ring is no longer a widely used LAN technology

## Slide 58: Fiber Distributed Data Interface Technology
FIDDI uses a token-passing access method and dual rings for redundancy
  Usually a physical ring of fiber-optic cable
FIDDI transmits at 100 Mbps and can include up to 500 nodes over a distance of 60 miles
  FIDDI full-duplex technology can support up to 200 Mbps
An FIDDI network has no hubs
  Devices called “concentrators” can server as a central connection point for buildings or sites in a campus setting
Obsolete on new networks

## Slide 59: Summary
Networks can be described by a physical and logical topology
  Physical topology describes the arrangement of cabling that connects one device to another
  Logical topology describes the path data travels between devices
The main physical topologies are the bus, star, ring, and point-to-point
  A star topology, along with the extended star, is the most common for implementing LANs
The main logical topologies are bus, ring, and switched
A network technology defines the structure of the frames and how a network interface access the medium to send data frames

## Slide 60: Summary
The most common network technology for LANs is Ethernet
Wi-Fi is a wireless technology based on Ethernet but uses the CSMA/CA media access method
The antenna on a Wi-Fi device is both the transmitter and receiver
Wi-Fi signal interference can severely affect a WLAN’s performance and reliability
Token Ring and FDDI are both obsolete technologies that used a token passing access method