## Slide 1: Network Media
Topic 6B

## Slide 2: Learning Outcomes
By the end of this lesson, you should be able to:
Define the primary cables used in wired networking
Describe the characteristics of the major types of fiber-optic media
Explain the technologies used for wireless networking

## Slide 3: Wired Networking
Wired networking uses tangible physical media called “cables”
Two broad categories of cables are copper wire and fiber optic
The main differences between the two types:
  Composition of signals (electricity or light)
  Speed at which signals can be sent
  Distance the signals can effectively travel

## Slide 4: Criteria for Choosing Network Media
Bandwidth Rating
  Bandwidth is the number of bits per second that can be transmitted across a medium
  A factor determining bandwidth is how bit signals are represented on the medium (called encoding)
  When possible, choose a cabling category that’s compatible with the standard you want to implement now but will support growth and faster speeds
Maximum Segment Length
  A cable segment is a length of cable between two network devices
    Intermediate passive devices, such as wall jacks, are considered part of the total segment length
  Each cable type can transport data only so far before its signals begin to weaken beyond what can be read by a receiving device (called attenuation)

## Slide 5: Criteria for Choosing Network Media
Interference and Eavesdropping Susceptibility
  Interference to electrical signals on copper media comes in the form of electromagnetic interference (EMI) and radio frequency interference (RFI)
    Motors, transformers, fluorescent lights and other sources of intense electrical activity can emit both EMI and RFI.
    RFI can also affect wireless networks if the frequencies are in the same range
  Crosstalk is interference one wire generates on another wire when both wires are in a bundle
  Copper wire is susceptible to electronic eavesdropping
  Fiber-optic media carries light signals and is not susceptible to interference or eavesdropping

## Slide 6: Criteria for Choosing Network Media
Cable Grade
  Building and fire codes include specific cabling requirements
  Cables ran between a false ceiling and the true ceiling (plenum) must be plenum-rated
  UTP cabling is marked as communications riser (CMR) or communications plenum (CMP)
  CMR can only be used for building risers or in cable trays
  CMP is suitable for use in plenum spaces
Connection Hardware
  Every type of cable has connectors that influence the kinds of hardware the cable can connect to
  You must make sure the media you select can be supported by the network device

## Slide 7: Criteria for Choosing Network Media
Other Media Considerations
  Ease of installation – factors to consider:
    Media’s minimum bend radius, which limits the angle at which a cable can be bent to run around corners
    Cost and time needed to terminate the medium
    Physical environment – types of walls and ceilings, EMI or RFI
  Testability – A network that “works” might be crippled by excessive errors
    It is important to certify whether the cable meets requirements for its category
  Total cost – includes cabling, connectors, termination panels, wall jacks, termination tools, testing equipment and time

## Slide 8: Coaxial Cable
Coaxial cable is often called “coax” for short
  Once was the predominant form of network cabling
Inexpensive and easy to install
Coax started to phase out in the early 1990’s
Today, coaxial cable is used primarily in connecting a cable modem to the wall outlet your cable TV/Internet provider installs

## Slide 9: Twisted-Pair Cable
Twisted-pair (TP) cable comes in two types: unshielded and shielded (UTP and STP)
TP consists of one or more pairs of insulated strands of copper wires twisted around one another and housed in an outer jacket
Twists are necessary to improve resistance to crosstalk from wires and EMI from outside sources
  The more twists per unit length, the better resistance to EMI and crosstalk
  More expensive TP is twisted more than less expensive and provides a better pathway for higher bandwidth networks

## Slide 10: Twisted-Pair Cable

## Slide 11: Twisted-Pair Cable
Unshielded Twisted-Pair Cable
  Most networks use Unshielded Twisted-Pair (UTP)
  UTP consists of four pairs of insulated wires
  It is rated according to categories devised by the Telecommunications Industry Association (TIA) and Electronic Industries Alliance (EIA) and American National Standards Institutes (ANSI)
  Categories 1 – 6a and Category 8 are accepted in US
  Two additional categories aren’t yet TIA/EIA standards and might never be in US
    Europe has accepted Category 7 and 7a, which specify that each wire pair is shielded
  Categories 5e and 6 are the most installed categories of UTP cabling
    Table 4-2 on the following slide shows Cat 5e and 6 UTP cabling characteristics

## Slide 12: Twisted-Pair Cable
Characteristic | Value
Maximum cable length | 100 m (328 ft)
Bandwidth | Up to 1000 Mbps
Bend radius | Minimum four times the cable diameter or 1 inch
Installation and maintenance | Easy to install, no need to reroute; the most flexible
Cost | Least expensive of all cabling options
Connector type | RJ-45 plug, RJ-45 jack, and patch panels
Security | Moderately susceptible to eavesdropping
Signaling rates | 100 MHz for Cat 5e; 250 MHz for Cat 6
Interference rating | Susceptible to EMI and crosstalk

## Slide 13: Twisted-Pair Cable
Shielded Twisted-Pair Cable
  STP includes shielding to reduce crosstalk and interference
    STP has a wire braid inside the sheath material or a foil wrap
  It is best to use STP in electrically noisy environments or for very high-bandwidth applications
  STP versions Cat 5e, Cat 6, and Cat 6a
    Sometimes referred to as “foiled twisted pair (FTP)”

## Slide 14: Twisted-Pair Cable

## Slide 15: Twisted-Pair Cable
Twisted-Pair Cable Plant Components
  RJ-45 Connectors – most STP and UTP cabling uses registered jack 45 (RJ-45)
    RJ-45 connectors are most commonly used in patch cables, which are used to connect computers to hubs, switches, and RJ-45 wall jacks
  Patch cable – short cable for connecting a computer to an RJ-45 wall jack or connecting a patch-panel port to a switch or hub
    Can be made with inexpensive tools, two RJ-45 plugs and a length of TP cable
  RJ-45 jacks – an RJ-45 jack is what you plug an RJ-45 connector into when the computer is in a work area away from hubs and switches
    RJ-45 jacks are usually placed behind wall plates when cables are run inside walls but can be recessed into the floor or placed in surface-mounted boxes

## Slide 16: Twisted-Pair Cable

## Slide 17: Twisted-Pair Cable

## Slide 18: Twisted-Pair Cable

## Slide 19: Twisted-Pair Cable
Twisted-Pair Cable Plant Components (continued)
  Patch Panels – used to terminate long runs of cable from where the computers are to the wiring closet (where the switches and hubs are)
  Distribution racks – hold network equipment such as routers and switches, plus patch panels and rack-mounted servers
    Also called 19” racks because the upright rails are 19” apart

## Slide 20: Twisted-Pair Cable

## Slide 21: Twisted-Pair Cable

## Slide 22: Structured Cabling: Managing and Installing a UTP Cable Plant
Structured cabling specifies how cabling should be organized, regardless of the media type or network architecture
Large networks typically use most or all of these:
  Work area
  Horizontal wiring
  Telecommunication closets
  Equipment rooms
  Backbone or vertical wiring
  Entrance facilities

## Slide 23: Structured Cabling: Managing and Installing a UTP Cable Plant
Work Area
  The work area is where workstations and other user devices are located
  Faceplates and wall jacks are installed in the work area
  Patch cables connect computers and printers to wall jacks
Horizontal Wiring
  Horizontal wiring runs from the work area’s wall jack to the telecommunication closet
  Wiring from the wall jack to the patch panel should be no longer than 90 meters (plus 10 meters for patch cables)

## Slide 24: Structured Cabling: Managing and Installing a UTP Cable Plant

## Slide 25: Structured Cabling: Managing and Installing a UTP Cable Plant
Telecommunications Closet
  The telecommunications closet (TC) provides connectivity to computer equipment in the nearby work area
  Typical equipment includes patch panels to terminate horizontal wiring runs, hubs and switches
  A TC that houses the cabling and devices for work area computers is referred to as an intermediate distribution frame (IDF)

## Slide 26: Structured Cabling: Managing and Installing a UTP Cable Plant

## Slide 27: Structured Cabling: Managing and Installing a UTP Cable Plant
Equipment Rooms
  The equipment room houses servers, routers, switches, and other major network equipment and serves as a connection point for backbone cabling
    An equipment room that’s the connection point between IDFs is called a main distribution frame (MDF) or “main cross-connect”
    An MDF can be the main cross-connect for the entire network or it might serve as the connecting point for backbone cabling between buildings
    Each building often has its own MDF

## Slide 28: Structured Cabling: Managing and Installing a UTP Cable Plant
Backbone Cabling
  Backbone cabling interconnects IDFs and MDFs
    This cabling runs between floors or wings of a building and between buildings
    It is often fiber-optic cable but can also be UTP if the distance between TCs is less than 90 meters
Entrance Facility
  Entrance Facility is the location of the cabling and equipment that connects a corporate network to a third-party telecommunications provider
    It can also serve as an equipment room and the main cross-connect for all backbone cabling
    Also where a connection to a WAN is made
    Demarcation point is the point where corporate LAN equipment ends and a third-party provider’s equipment and cabling begins

## Slide 29: Structured Cabling: Managing and Installing a UTP Cable Plant

## Slide 30: Structured Cabling: Managing and Installing a UTP Cable Plant
Installing UTP Cabling
  Cable termination means putting RJ-45 plugs on the ends of cable or punching down wires into terminal blocks on a jack or patch panel
  Some tools needed to create a patch panel and terminate cable:
    Bulk UTP cabling
    Wire cutters
    Cable Stripper
    Crimping Tool
    Type 110 punchdown tool
    Cable Tester
    RJ-45 plugs/jacks and patch panel

## Slide 31: Structured Cabling: Managing and Installing a UTP Cable Plant

## Slide 32: Structured Cabling: Managing and Installing a UTP Cable Plant
Installing UTP Cabling (continued)
  When making a cable or terminating a cable at a jack or patch panel it is important to get the colored wires arranged in the correct order
  There are two standards: TIA/EIA 568A and TIA/EIA 568B (see Figure 4-12 on the following slide)

## Slide 33: Structured Cabling: Managing and Installing a UTP Cable Plant

## Slide 34: Structured Cabling: Managing and Installing a UTP Cable Plant
Straight-Through versus Crossover Cable
  Standard patch cables are called straight-through cables (same wiring standard on both ends)
  Crossover cables – use 568A standard on one side of the cable and 568B standard on the other side
    Crosses the transmit and receive wires so that transmit on one end connects to receive on the other
    This type of cable is often needed when you connect two devices of the same type to one another
    For a 1000BaseT crossover cable, you have to cross the blue and brown pins because they’re used in 1000BaseT
  The following slide shows the pinout for a 1000BaseT crossover cable

## Slide 35: Structured Cabling: Managing and Installing a UTP Cable Plant
Pin | Connector 1 | Connector 2
1 | White with orange stripe | White with green stripe
2 | Orange | Green
3 | White with green stripe | White with orange stripe
4 | Blue | White with brown stripe
5 | White with blue stripe | Brown
6 | Green | Orange
7 | White with brown stripe | Blue
8 | Brown | White with blue stripe

## Slide 36: Structured Cabling: Managing and Installing a UTP Cable Plant
Medium Dependent Interface
  Network devices that connect by using RJ-45 plugs over twisted-pair cabling are classified as medium dependent interface (MDI) devices or MDI crossed (MDI-X) devices
  MDI devices transmit on pins 1 and 2 and receive on pins 3 and 6
    PC NICs and routers are examples
  MDI-X devices receive on pins 1 and 2 and transmit on pins 3 and 6
    Usually hubs and switches are examples
  When two switches (or any other like devices) need to be connected, you use a crossover cable so that transmit and receive wires get crossed
  Some devices have “auto-sensing” ports that can detect whether you are trying to connect transmit wires to transmit wires
    The port can reconfigure transmit and receive wires, making a crossover cable unnecessary

## Slide 37: Structured Cabling: Managing and Installing a UTP Cable Plant
Why Two Transmit and Two Receive Wires?
  One wire pair is used for transmit (labeled transmit+/transmit-) and one pair for receive (labeled receive+/receive-)
  The plus and minus symbols indicate that the wires carry a positive or a negative signal
  This differential signal mitigates the effect of crosstalk and noise on the cable

## Slide 38: Fiber-Optic Cable
With fiber-optic cable, bits are transmitted as pulses of light instead of electricity
  Makes it immune to electrical interference
Fiber-optic cable is highly secure because electronic eavesdropping is eliminated
Composition of fiber-optic cable:
  A slender cylinder of glass fiber called the core is surrounded by a concentric layer of glass called the cladding
  Fiber is then jacketed in a thin transparent plastic material called the buffer
In most cases, each fiber-optic strand carries data in only one direction
  Network connections typically consist of two or more strands

## Slide 39: Fiber-Optic Cable

## Slide 40: Fiber-Optic Cable
Fiber-optic cable used as backbone cabling often comes in bundles of 12 or more fiber strands
  Even if you are only using 2 in the backbone, running more is a good idea so that you are ready for any future expansion
Some testing has shown that glass fibers can carry several terabits (1000 gigabits) per second
  Fiber-optic cable may one day replace copper for all types of network connections
Table 4-5 on the following slide summarizes fiber-optic characteristics

## Slide 41: Fiber-Optic Cable
Characteristic | Value
Maximum cable length | 2 km (6562 ft) to 100 km (62.14 miles)
Bandwidth | 10, 40, and 100 Gbps and higher
Bend radius | 30 degrees per foot
Installation and maintenance | Difficult to install and reroute; sensitive to strain and bending
Cost | Most expensive of all cabling options
Connector type | Several types (see bulleted list in the next section)
Security | Not susceptible to eavesdropping
Interference rating | None; least susceptible of all cable types

## Slide 42: Fiber-Optic Connectors
Types of connectors:
  Straight connection (SC)
  Straight tip (ST)
  Mechanical transfer registered jack (MT-RJ)
  Locking connection (LC)
  Fiber channel or ferrule connector (FC)
  Medium interface connector (MIC)
  Subminiature type A (SMA)

## Slide 43: Fiber-Optic Installation
Installing fiber-optic networks is more difficult than installing copper media
  However, advances in connector technology are closing the gap
Connectors and test equipment required for termination are still more expensive than copper
There are many methods for terminating fiber-optic cables because of the many connectors and cable types available
  Installation details are beyond the scope of this book
Some tools in a typical fiber-optic termination kit include:
  Buffer tube stripper and cable stripper
  Crimper
  Diamond cleaver
  Inspection scope
  Polishing tool

## Slide 44: Fiber-Optic Cable Types
Single-mode fiber (SMF):
  Includes a single, small-diameter fiber at the core (8 microns)
  Generally works with laser-based emitters
  Spans the longest distances
  Used in higher-bandwidth applications
Multimode fiber (MMF) :
  Larger diameter fiber at the core (50 and 62.5 microns)
  Costs less than SMF
  Works with lower-power light emitting diodes (LEDs)
  Spans shorter distances

## Slide 45: Cable-Testing Equipment
Common tools for testing and troubleshooting wired networks:
  Cable certifier
  Basic cable tester
  Tone generator
  Time domain reflectometer (TDR)
  Multimeter
  Optical power meter (OPM)

## Slide 46: Wireless Networking
Demand for wireless networking has increased considerably
  Production of wireless equipment has increased, which brings prices down
Wireless networks are often used with wired networks to interconnect geographically dispersed LANs or groups of mobile users with wired servers and resources on a wired LAN (sometimes referred to as “hybrid networks”)
Even in small networks with workstations connecting to a wireless AP or router, the AP or router usually connects to the Internet via a wired connection to a cable modem

## Slide 47: Wireless Benefits
Wireless networking can offer the following capabilities:
  Create temporary connections to wired networks
  Establish backup or contingency connectivity for existing wired networks
  Extend a network’s span beyond the reach of wire-based or fiber-optic cabling, especially in older buildings where rewiring might be too expensive
  Allow businesses to provide customers with wireless networking easily, offering a service that gets customers in and keeps them there
  Enable users to roam around an organization or college campus with their devices

## Slide 48: Wireless Benefits
Common applications for wireless networking technologies include:
  Ready access to data for mobile workers
  Delivering network access to isolated facilities or disaster-stricken areas
  Access in environments where layout and settings change constantly
  Improved customer services in busy areas, such as check-in or reception centers
  Network connectivity in structures where in-wall wiring is impossible to install or prohibitively expensive
  Home networks where running cables is inconvenient

## Slide 49: Types of Wireless Networks
Wireless networks can be subdivided into the following categories:
  Local area networks (LANs) – usually provides connectivity for mobile users or across areas that couldn’t otherwise be networked
  Extended LANs – usually used to increase a LAN’s span beyond normal distance limitations
  Internet service – used to bring Internet access to homes and businesses
  Mobile computing – users communicate by using a wireless networking medium that enable them to move while remaining connected to a network

## Slide 50: Wireless LAN Components
The wireless components of most LANs behave like their wired counterparts
Network interface attaches to an antenna and an emitter rather than to a cable
Transceiver or an access point (AP) is a transmitter/receiver device that must be installed to translate between wired and wireless networks
  Includes an antenna and a transmitter to send and receive wireless traffic but also connects to the wired side of the network
  Shuttles traffic back and forth between a network’s wired and wireless sides

## Slide 51: Wireless LAN Transmission
Wireless communications depends on sending and receiving signals broadcast through the air to carry information
  These signals take the form of waves in the electromagnetic (EM) spectrum
  The frequency of the wave forms used for communication is measured in cycles per second, usually expressed as hertz (Hz)
Lower-frequency transmissions can carry less data more slowly over longer distances, and higher-frequency transmissions can carry more data faster over shorter distances
The following are the most common frequencies for wireless data communication:
  Radio – 10 KHz to 300 MHz
  Microwave – 300 MHz to 300 GHz
  Infrared – 300 GHz to 400 THz (terahertz)

## Slide 52: Wireless LAN Transmission
Wireless LANs make use of four primary technologies for transmitting and receiving data
  Infrared
  Laser
  Narrowband (single-frequency) radio
  Spread-spectrum radio

## Slide 53: Wireless LAN Transmission
Infrared LAN Technologies
  Infrared (IR) wireless networks use infrared light beams to send signals between pairs of devices
    IR works well for LAN applications due to high bandwidth
  Four main kinds of infrared LANs include:
    Line-of-sight networks require an unobstructed view between transmitter and receiver
    Reflective wireless networks broadcast signals from optical transceivers near devices to a central hub
    Scatter infrared networks bounce transmissions off walls and ceilings to deliver signals
    Broadband optical telepoint networks provide broadband services

## Slide 54: Wireless LAN Transmission
Laser-Based LAN Technologies
  Laser-based transmissions also require a clear line of sight between sender and receiver
  Laser-based LAN devices are subject to many of the same limitations as infrared
  Aren’t as susceptible to interference from visible light sources as infrared
Narrowband Radio LAN Technologies
  Use low-powered, two-way radio communication
  The receiver and transmitter must be tuned to the same frequency Requires no line of sight between sender and receiver as long as both parties stay within the broadcast range of these devices
    Typically 70 meters or 230 feet
  Depending on the frequency, walls or other solid barriers can block signals
  Interference from other radio sources is possible
  Table 4-6 (see next slide) displays narrowband wireless LAN characteristics

## Slide 55: Wireless LAN Transmission
Characteristic | Value
Frequency ranges | Unregulated: 902-928 MHz, 2.4 GHz, 5.72-5.85 GHz
Maximum distance | 50-70 m (164-230 ft)
Bandwidth | 1-10 Mbps
Installation and maintenance | Easy to install and maintain
Interference | Highly susceptible
Cost | Moderate
Security | Highly susceptible to eavesdropping within range

## Slide 56: Wireless LAN Transmission
Spread-Spectrum LAN Technologies
  Spread-spectrum uses multiple frequencies simultaneously, improving reliability and reducing susceptibility to interference
    Also makes eavesdropping more difficult
  Two main kinds of spread-spectrum communications:
    Frequency hopping – switches data between multiple frequencies at regular intervals
    Direct-sequence modulation – breaks data into fixed-size segments called chips and transmits the data on several different frequencies at the same time
  Table 4-8 on the following slide displays spread-spectrum LAN characteristics

## Slide 57: Wireless LAN Transmission
Characteristic | Value
Frequency ranges | Unregulated: 902-928 MHz or 2.4 GHz, 5 GHz
Maximum distance | Limited to cell boundaries but often extends over several miles
Bandwidth | 1-2 Mbps for frequency hopping, 2-6 Mbps for direct-sequence modulation
Installation and maintenance | Depends on equipment; ranges from easy to difficult
Interference | Moderately resistant
Cost | Inexpensive to moderate
Security | Not very susceptible to eavesdropping

## Slide 58: LAN Media Selection Criteria
In LANs, there are three main media choices: UTP, fiber-optic, and wireless
When choosing between media types, consider:
  Bandwidth – Higher bandwidth means more expensive cable and higher installation costs
    If 40 Gbps or more, fiber-optic is the only choice
  Budget – A typical UTP cable installation cost $100 - $200 per cable run and fiber-optic might cost twice that much
    Wireless have no physical installation costs but you need to install access points and verify connectivity
  Environmental considerations – How electrically noisy is the environment? How important is data security?
    The more weight either factor has, the more likely fiber-optic or secured wireless is the right choice

## Slide 59: LAN Media Selection Criteria
When choosing between media types, consider (continued):
  Span – What kind of distance must the network span?
    Longer spans might require fiber-optic or wireless be used between buildings
    Strategic placement of small switches or hubs gives UTP surprising reach
  Existing cable plant – For an upgrade, the existing cable plant must be considered
Table 4-9 on the following slide condenses the most important information for the cable types covered in this chapter

## Slide 60: LAN Media Selection Criteria
Type | Maximum cable length | Bandwidth | Installation | Interference | Cost
UTP | 100 m | 10-10,000 Mbps | Easy | High | Cheapest
STP | 100 m | 16-10,000 Mbps | Moderate | Moderate | Moderate
Fiber optic | 2-100 km | 100 Mbps-10 Gbps | Moderate | None | Most expensive
Wireless | 100-300 ft | 11-300 Mbps | Easy | Moderate | None for physical media

## Slide 61: Summary
Wired networking media come in two primary categories: copper and fiber-optic
Twisted pair cabling comes in shielded or unshielded varieties
  Most use UTP, but STP can be used in electrically noisy environments
Twisted pair cabling components consist of connectors, patch cable, jacks, patch panels and distribution racks
A structured cabling plant consists of work areas, horizontal wiring, telecommunications closets (IDFs), equipment rooms (MDFs), backbone cabling, and entrance facilities
Fiber-optic uses pulses of light to represent bits and is immune to EMI, RFI and electronic eavesdropping

## Slide 62: Summary
Wireless networks can be subdivided into LANs, extended LANs, and mobile computing
Components of a wireless LAN are a NIC, an antenna, and a transceiver or access point
Technologies used to transmit and receive data including: infrared, laser, narrowband radio and spread-spectrum radio
Criteria for choosing LAN media include needed bandwidth, budget, environmental factors, the distance the network must span, and the existing cable plant
Networks combining fiber-optic, UTP, and wireless have become the norm