## Slide 1: Network Protocols
Topic 8B

## Slide 2: Learning Outcomes
By the end of this lesson, you should be able to:
Describe TCP/IP Transport-layer
Describe TCP/IP Internetwork-layer
Describe TCP/IP Network access layer

## Slide 3: Transport Layer
TCP/IP

## Slide 4: Transport-Layer Protocols
Transport-layer protocols are used with most Application-layer protocols because they:
  Supply a header field to identify the Application layer
  Provide reliability and flow control for applications that typically transfer a large amount of data

## Slide 5: Role of the Transport Layer
The Transport layer has two protocols:
  Transmission Control Protocol (TCP) is connection oriented and designed for reliable transfer of information in complex internetworks
  User Datagram Protocol (UDP) is connectionless and designed for efficient communication of generally small amounts of data
  Both protocols perform the following tasks:
    Work with segments (TCP) or datagrams (UDP)
    Provide a means to identify the source and destination applications involved in a communication
    Protect data with a checksum

## Slide 6: Role of the Transport Layer
Working with Segments and Datagrams
  TCP works with units of data called “segments” and UDP work with units of data called “datagrams”
  Both TCP and UDP add a header to data
  The Transport-layer protocol then passes the segment to the Internetwork-layer protocol (usually IP)
  With incoming data, the Internetwork-layer protocol de-encapsulates the packet and forwards the resulting segment or datagram to the Transport-layer protocol
    The Transport-layer protocol processes it, de-encapsulates it, and sends the resulting data up to the Application layer

## Slide 7: Role of the Transport Layer
Identifying Source and Destination Applications
  How do computers keep track of incoming data when a Web browser, email application, chat and a word processing program are all running at the same time?
  TCP and UDP use port numbers to specify the source and destination Application-layer protocols
    Port numbers are 16-bit values assigned to specific applications running on a computer or network device
    The Internet Assigned Numbers Authority (IANA) assigns a dedicated port number to every well-known network service

## Slide 8: Role of the Transport Layer
Protecting Data with a Checksum
  To protect data integrity, TCP and UDP provide a checksum similar to the CRC
  Intermediate devices don’t recalculate the checksum in the Transport layer so if data corruption occurs during the transmission, the final receiving station detects the checksum error and discards the data

## Slide 9: TCP: The Reliable Transport Layer
If an application requires reliable data transfer, it uses TCP as the Transport-layer protocol
TCP provides reliability by using these features that aren’t available in UDP:
  Establishing a connection
  Segmenting large chunks of data
  Ensuring flow control with acknowledgements
TCP is a connection-oriented protocol
  It establishes a connection with the destination, data is transferred, and the connection is broken

## Slide 10: TCP: The Reliable Transport Layer
Establishing a Connection: The TCP Handshake
  A TCP session begins when a client sends a TCP synchronization (SYN) segment to the destination device, usually a server
    A destination port is specified and a source port is assigned dynamically
  When the server receives the SYN segment, it responds by sending either an acknowledgement-synchronization (ACK-SYN) segment or a reset connection (RST) segment
    An RST is sent when the server refused the request to open the session
    If an ACK-SYN is returned, the client completes the three-way handshake by sending an ACK segment back to the server

## Slide 11: TCP: The Reliable Transport Layer
Segmenting Data
  When TCP receives data from the Application layer, the size might be too large to send in one piece
  TCP breaks the data into smaller segments (max frame sent by Ethernet is 1518 bytes)
  Each segment is labeled with a sequence number so that if segments arrive out of order they can be reassembled in the correct order

## Slide 12: TCP: The Reliable Transport Layer
Ensuring Flow Control with Acknowledgments
  Flow control prevents a destination from becoming overwhelmed by data, resulting in dropped packets
  TCP establishes a maximum number of bytes, called the “window size”, that can be sent before the destination must acknowledge the receipt of data
  If no acknowledgement is received within a specified period of time, the sending station will retransmit from the point at which an acknowledgement was last received

## Slide 13: Internetwork Layer
TCP/IP

## Slide 14: Internetwork-Layer Protocols
The Internetwork layer is where administrators usually do the most network configuration
This layer is where the IP protocol operates and is the heart of the TCP/IP protocol suite
The Internetwork layer is responsible for four main tasks:
  Defines and verifies IP addresses
  Routes packets through an internetwork
  Resolves MAC addresses from IP addresses
  Delivers packets efficiently

## Slide 15: Defines and Verifies IP Addresses
An IP address is assigned to every computer and network device using TCP/IP for communications
IP addresses are used for two main purposes:
  To identify a network device at the Internetwork layer
  To identify the network on which a device resides
When a device receives an IP packet, it compares the destination IP address with it’s own:
  If it matches or is a broadcast, the packet is processed
  It is does not match then it is discarded
Every IP address contains two parts:
  A network ID
  A host ID

## Slide 16: Routes Packets through an Internetwork
The Internetwork layer determines the best way to get a packet from network to network until it reaches its destination
Most large internetworks (the Internet) have multiple paths for getting from one network to another
Routers work at the Internetwork layer and it is their job to select the best path to the destination
  Routers use the network ID portion of IP addresses along with their routing tables to determine the best path

## Slide 17: Resolves MAC Addresses from IP Addresses
Every frame contains both physical (MAC) and logical (IP) source and destination addresses
When a packet is ready to be sent to the Network access layer, the destination device’s MAC address must be retrieved before the frame header can be constructed
TCP/IP uses Address Resolution Protocol (ARP) to find MAC addresses
  ARP is discussed in more detail later in the chapter

## Slide 18: Delivers Packets Efficiently
Internetwork-layer protocols primarily focus on efficient delivery of packets
  Features such as flow control, delivery confirmation or message assembly are not included in Internetwork-layer protocols
    These features require overhead to ensure reliable delivery
Internetwork-layer protocols rely on the protocols in the Transport and Application layers to provide reliability features
  Is considered a connectionless protocol, which relies on upper-layer protocols to ensure the packet’s safe journey

## Slide 19: Protocols at the Internetwork Layer
Some of the most commonly used Internetwork-layer protocols:
  IPv4
  IPv6
  ARP
  ICMP
  IPsec

## Slide 20: Protocols at the Internetwork Layer
Internet Protocol Version 4
  IPv4 is also known as “IP”
  IPv4 is the most common version in networks and the first version that was in widespread use
  It defines a 32-bit dotted decimal IP address
    Example: 172.31.149.10
  Important fields in an IP packet:
    Version
    Time to live (TTL)
    Protocol
    Checksum
    Source and Destination address

## Slide 21: Protocols at the Internetwork Layer

## Slide 22: Protocols at the Internetwork Layer
Internet Protocol Version 6
  Uses a different format for IP addresses than IPv4
  IPv6 can run alongside IPv4 without needing to change the Transport Layer or Network Access Layer
  Improvements and changes from IPv4:
    Larger address space
    Hierarchical address space
    Autoconfiguration
    Built-in Quality of Service (QoS) support
    Built-in support for security
    Support for mobility
    Extensibility

## Slide 23: Protocols at the Internetwork Layer
Address Resolution Protocol
  Address Resolution Protocol (ARP) is used to resolve a logical (IP) address to physical (MAC) address
    When a source doesn’t have the destination’s MAC it sends out an ARP broadcast frame requesting the MAC address corresponding to the host’s IP address
    A network device configured with the specified IP address responds with an ARP reply containing its MAC address
  To avoid sending an ARP request every time, PCs and other devices store learned IP address/MAC address pairs in an ARP cache which is a temporary location in RAM

## Slide 24: Protocols at the Internetwork Layer
Address Resolution Protocol (continued)
  If the destination computer is on another network:
    The computer uses ARP to retrieve the MAC address of the router configured as its default gateway
    The packet is delivered to the router and the router determines where the packet should go next to get to its destination

## Slide 25: Protocols at the Internetwork Layer

## Slide 26: Protocols at the Internetwork Layer
Internet Control Message Protocol
  Internet Control Message Protocol (ICMP) is used to send error, status, and control messages between systems or devices
  ICMP is a specialized IP packet with its own header
  The ping program uses ICMP Echo packets to request a response from another computer or to verify whether it is available for communication
  A ICMP Echo Reply packet indicates whether the host is reachable and how long the message’s round trip from sender to receiver took
  The tracert program uses ICMP Echo packets to determine the route a packet takes through an internetwork

## Slide 27: Protocols at the Internetwork Layer
Internet Protocol Security
  Internet Protocol Security (IPsec) works with IPv4 to ensure secure delivery of packets
  IPsec can be used to secure sensitive network transmissions between computers that need extra security
  This protocol provides security by using authentication and encryption
  IPsec requires additional network/computer resources, so it should be enabled only for highly sensitive communication and in environments where security risks are high

## Slide 28: Network Access Layer
TCP/IP

## Slide 29: Network Access Layer
Some tasks performed by the Network access layer:
  Provides a physical (MAC) address for the network interface
  Verifies incoming frames have the correct destination MAC address
  Defines and follows media access rules
  Receives packets from the Internetwork layer and encapsulates them to create frames
  De-encapsulates received frames and sends the resulting packets to the Internetwork layer
  Often provides frame error detection in the form of a CRC code
  Transmits and receives bit signals
  Defines the signaling needed to transmit bits, whether electrical, light pulses, or radio waves
  Defines the media and connectors needed to make a physical network connection

## Slide 30: Network Access Layer

## Slide 31: Summary
TCP/IP is the main protocol suite used in networks
  TCP/IP takes a layered approach and is organized in four layers
The Transport layer provides reliability and works with segments (TCP) and datagrams (UDP)
  Transport-layer protocols supply a header field to identify the Application layer and provide reliability and flow control
The Internetwork layer is where most network configuration occurs and is composed of IP, ICMP, and ARP
  This layer is responsible for four main tasks: defining and verifying IP addresses, routing packets through an internetwork, resolving MAC addresses from IP addresses, and delivering packets efficiently
The Network access layer is composed of network technologies, such as Ethernet and WAN technologies
  Some tasks performed include providing a physical (MAC) address for the network interface, verifying that incoming frames have the correct destination MAC address, receiving packets from the Internetwork layer and encapsulating them to create frames, and transmitting and receiving bit signals